ESC Host Adapter Supplement
			Release	and Installation Notes
				Version	1.2.0
			       15 December 1990




    1.	Preface

    The	ESC Host Adapter Supplement provides your UNIX(r) System with the
    following:

       o an EISA (extended industry standard architecture) SCSI	device
	 driver	that enables your computer to use the full capabilities	of
	 the EISA bus SCSI controller.	(A device driver is a special pro-
	 gram that is installed	in the UNIX operating system to	allow pro-
	 grams and commands to be sent to or received from a hardware dev-
	 ice.)

       o a standby power supply	(SPS) package that allows your computer	to
	 continue working when power has failed	if your	system contains
	 the optional SPS power	unit.  The SPS package includes	an SPS
	 background program (called a daemon).	This daemon is automati-
	 cally invoked when your computer is brought from single-user to
	 multiuser mode	at boot	time.  It detects A/C power failures and
	 safely	shuts down the system while it is running on battery
	 power.	 In addition, the daemon writes	messages to the	front
	 panel display to keep the operator apprised of	power conditions.
	 When installed, the daemon is stored in the /etc/sps_daem file.
	 The /etc/rc2.d/S49sps file starts this	daemon.

       o a device driver that permits messages to be written to	the front
	 panel display of your computer	(if you	have installed the ESC
	 Host Adapter Supplement on a CP486 computer). The device file
	 that is created is /dev/front_	panel.	This device allows the SPS
	 package to monitor the	status of the power supply.  You can also
	 use this device name to write simple test messages to verify suc-
	 cessful installation.	The command for	this test is described
	 later in the ``Testing	the Installation'' section.


    2.	Configuration Requirements

    You	need the following resources to	install	and run	the ESC	Host
    Adapter Supplement:















    15 December	1990		    - 1	 -  The	Santa Cruz Operation, Inc.


    Release Notes


		    ______________________________________
		    |COMPUTER	   | DEC DS425 or	  |
		    |		   | Olivetti EISA Sys-	  |
		    |		   | tems CP486	or M486	  |
		    |______________|______________________|
		    |OPERATING	   | UNIX System V/386	  |
		    |SYSTEM	   | Release 3.2v2.0 or	  |
		    |		   | SCO Open Desktop (r) |
		    |		   | Release 1.0.0 or SCO |
		    |		   | Open Desktop Release |
		    |		   | 1.1.0 (with Update	  |
		    |		   | F)			  |
		    |______________|______________________|
		    |DISK CAPACITY | No	additional	  |
		    |		   | storage space is	  |
		    |		   | needed for	this sup- |
		    |		   | plement		  |
		    |______________|______________________|
		    |RAM	   | No	additional RAM is |
		    |		   | needed for	this sup- |
		    |		   | plement		  |
		    |______________|______________________|



    3.	Installing the ESC Host	Adapter	Supplement

    After you have installed SCO UNIX System V/386 Release 3.2v2.0 or SCO
    Open Desktop Release 1.0.0 or 1.1.0, follow	the steps outlined in the
    following procedure	to install the ESC Host	Adapter	Supplement using
    the	custom utility.	 You should install the	ESC Host Adapter Supple-
    ment after you install the operating system	installation but before
    you	install	any other software.

    *********************************************************************
    NOTE

    If you have	already	installed Open Desktop 1.0 with	Maintenance Sup-
    plement UFE, please	refer to the section ``Installation Order with
    Open Desktop and UFE'' later in these notes	for special installation
    instructions.
    *********************************************************************


    During this	installation procedure,	if you have previously configured
    a Keyboard Mouse for use on	your system (such as during the	installa-
    tion of Open Desktop), you are prompted if you want	to change the
    reference from Keyboard Mouse to Olivetti New Advanced Mouse.  Change
    the	reference if you are using an Olivetti New Advanced Mouse to allow
    the	software to conform to Olivetti	documentation.	Changing the
    reference has no effect on mouse performance.

    You	are not	prompted to change the reference if there is no	Keyboard
    Mouse configured on	the system.  However, the init script adds the
    Olivetti New Advanced Mouse	to the list of mouse drivers that are
    supported by the mkdev mouse utility.




    15 December	1990		    - 2	 -  The	Santa Cruz Operation, Inc.


					       ESC Host	Adapter	Supplement

    To install the ESC Host Adapter Supplement,	follow these steps:

      1.  Reboot the system and	enter single-user mode.	 You must be in
	  single-user mode to install the ESC Host Adapter Supplement.

      2.  Type custom and press	<Return>.  Select Install from the initial
	  custom menu, then select A New Product from the next menu.

      3.  Choose the menu selection Entire Product from	the displayed
	  menu.	 This selection	installs the ESC Host Adapter Supplement
	  operating system supplement package.

      4.  You are prompted to insert Distribution Volume 1.  Insert the
	  ESC Host Adapter Supplement diskette into floppy drive 0 and
	  press	<Return> to continue.  You see the messages Installing
	  custom data files...,	Executing Product Prep Script, and Creat-
	  ing file lists....

      5.  You are prompted to insert the ESC Host Adapter Supplement
	  Volume 1.  Because you have already inserted it, press <Return>
	  to continue.

      6.  If you are installing	on Open	Desktop, you see a copyright mes-
	  sage after the volume	is extracted.  You are prompted	to enter
	  the serial number and	the activation key.  Enter the same number
	  and key that were supplied with the operating	system.

	  If you are not installing on Open Desktop, skip to the next
	  step.

      7.  This message is displayed:

	  EISA Driver Installation

	  The following	supplemental drivers will be
	  installed:
	  esc		- EISA SCSI adapter driver
	  fpan		- front	panel driver

	  The front panel driver requires that the Streams
	  driver be configured into the	kernel.	 The EISA
	  driver installation procedure	will configure
	  Streams automatically.

      8.  As the drivers are installed,	messages announcing that they were
	  added	are displayed.

      9.  If you have previously selected a Keyboard Mouse for use on your
	  system, you are shown	a list of terminals on which the Keyboard
	  Mouse	is configured for use. You are asked if	you want to change
	  all references from Keyboard Mouse to	Olivetti New Advanced
	  Mouse.

	  Enter	y if you want to change	the reference, n if you	want to
	  leave	the reference as Keyboard Mouse.






    15 December	1990		    - 3	 -  The	Santa Cruz Operation, Inc.


    Release Notes


     10.  You are prompted if you want to create a new kernel.

    *********************************************************************
    NOTE

    If you have	already	installed Open Desktop 1.0 with	Maintenance Sup-
    plement UFE, please	refer to the section ``Installation Order with
    Open Desktop and UFE'' for special installation instructions before
    relinking the kernel.
    *********************************************************************

	 Enter y.

     11.  This message is displayed:

	  The UNIX Operating System will now be	rebuilt.
	  This will take a few minutes.	 Please	wait.

	  You may also see this	message:

	warning: no dma	channel	specified for scsi device: prefix oha

	  You can ignore this warning, even if it is displayed more than
	  once.

     12.  You are prompted to decide if	the new	kernel is to boot by
	  default.  Enter y.

     13.  After	the operating system is	rebuilt, you are prompted to
	  decide if you	want the kernel	environment rebuilt.  Enter y.

     14.  The message Press any	key to continue	is displayed.  Press any
	  key.	You see	the message Checking file permissions.

     15.  The custom menu is displayed.	 Select	Quit to	leave the custom
	  menu,	and enter y to exit custom.

     16.  Remove the distribution volume from the floppy drive.

     17.  Type reboot and press	<Return>.


    4.	Installation Order with	Open Desktop 1.0 and UFE

    If you have	already	installed Open Desktop 1.0 and the Maintenance
    Supplement UFE on your system, follow this installation order:

      1.  Begin	installing the ESC Host	Adapter	Supplement.  When you are
	  prompted to relink the kernel, be sure to answer n.

      2.  Press	any key	to return to the custom	menu.

      3.  Use custom to	install	the Maintenance	Supplement UFE again.
	  Follow the instructions provided in the cover	letter that accom-
	  panies the supplement.  Note that you	can relink the kernel when
	  you are prompted to do so.




    15 December	1990		    - 4	 -  The	Santa Cruz Operation, Inc.


					       ESC Host	Adapter	Supplement

      4.  Exit from custom.

    You	can now	install	any other supplements.

    5.	Testing	the Installation

    You	can test the installation by using the front panel driver.  Enter
    this command to display the	phrase ``Hello,	World''	on the front
    panel:

	      echo -n "Hello, World" >>	/dev/front_panel

    If the message is displayed, the front panel driver	(and presumably
    the	rest of	the installation) was installed	successfully.

    If you do not have a front panel display, execute the same command.
    If you receive no error messages, then the installation was	success-
    ful.

    6.	Notes

    The	following sections describe issues you should be aware of concern-
    ing	the ESC	Host Adapter Supplement.

    6.1	 WARNING: Accessing Raw	Devices	on an ODT 1.0.0	and Update E
	 System

    If you are using SCO Open Desktop 1.0.0 and	you have Update	E
    installed on your system, you can access the raw device only in multi-
    ples of the	device's block size.  For a hard disk, this is 512 bytes.
    For	example, when using the	dd(C) utility on a hard	disk raw device,
    you	cannot use the bs=block_size option unless block_size is some mul-
    tiple of 512 bytes.

    Failure to heed this warning can result in freezing, or hanging, your
    system.  If	this occurs, you must reboot the system.

    This restriction does not apply if your system is running UNIX System
    V/386 Release 3.2v2.0 SCO Open Desktop 1.1.0, nor does it apply if
    your system	is running SCO Open Desktop 1.0.0 but you do not have
    Update E installed.

    6.2	 Reinstalling the Link Kit

    If you need	to reinstall the Link Kit after	you have installed the ESC
    Host Adapter Supplement, you must reinstall	the supplement before con-
    figuring the kernel.

    *********************************************************************
    NOTE

    Reinstalling the Link Kit if you are using Open Desktop 1.0	is not
    advised.
    *********************************************************************







    15 December	1990		    - 5	 -  The	Santa Cruz Operation, Inc.


    Release Notes

    6.3	 Relinking the Kernel

    Each time that you relink the kernel, you may see this message:

    warning: no	dma channel specified for scsi device: prefix oha

    You	can continue to	ignore this message.

    6.4	 Extended Memory Support

    If you are installing on an	Open Desktop 1.0.0 system, the ESC Host
    Adapter Supplement provides	extended memory	support.  The extended
    memory support allows your system to recognize and use up to 256 MB	of
    RAM.

    6.5	 Tape Drive Accessing Delay

    If you are installing the ESC Host Adapter Supplement on a machine
    with less than 4 megabytes (MB) of RAM, there is a two-minute delay	in
    accessing the tape drive.  This does not occur if you use 8	MB of RAM.


    7.	Selecting Boot and Root	Devices

    When your system boots, the	Basic Input/Output System (BIOS) searches
    for	a hard disk device, or boot device, from which to load the operat-
    ing	system.	 Once the BIOS passes control to the operating system, the
    operating system looks for its root	filesystem on a	hard disk, or root
    device.  The boot and root devices should match.

    The	BIOS uses a standard search sequence to	look for the boot device,
    first looking for a	WD1007-type controller,	then looking for other
    devices (such as a SCSI host adapter).  The	operating system dupli-
    cates this search sequence when locating the root device.

    Before you install the ESC Host Adapter Supplement,	the ESC-1 host
    adapter board emulates a WD1007-type controller by default,	for AT
    compatibility.  The	operating system finds this emulated WD	device
    first and uses the ESC-1 AT	compatibility mode for a boot device.
    This mode is a low-performance mode	that does not take advantage of
    SCSI or ESC-1 features.

    Installing the ESC host adapter supplement modifies	the system's
    default search sequence so that the	system searches	for SCSI devices
    first.  This new search sequence allows the	system to find ESC-1 and
    use	it as a	high-performance, SCSI host adapter.

    After you install the supplement, you can change the default so that
    the	search sequence	again looks for	WD1007-type controllers	first.
    You	need to	make this change if you	have both a WD1007-type	controller
    and	an ESC-1 host adapter on your system, to match the boot	and root
    devices.  After you	reset the search sequence to look for WD1007-type
    controllers	first, the WD disk is both the root and	boot device, and
    any	SCSI disks are secondary.







    15 December	1990		    - 6	 -  The	Santa Cruz Operation, Inc.


					       ESC Host	Adapter	Supplement

    To configure the system to boot using the WD disk driver, you must
    change the variable	root_on_Sdsk in	the file
    /etc/conf/pack.d/hd/space.c.  Use a	text editor, such as vi(C), to set
    this variable as follows:

       o Set the variable to 0 (zero) to boot using the	WD disk	drive or
	 to boot using the SCSI	disk in	AT Emulation mode if no	other
	 disks are present.

       o Set the variable to 1,	which is the default, to boot using a ESC
	 Disk Controller.

    After altering the variable	in the space.c file you	must relink the
    kernel to activate your changes.  To relink	the kernel, first change
    to the /etc/conf/cf.d directory:

	 cd /etc/conf/cf.d

    Enter the following	command	to relink the kernel:

	 ./link_unix



    8.	Advanced SPS Operation

    The	effects	of an unexpected power outage on a multiuser computer sys-
    tem	are substantially greater than for a standalone	system.	For that
    reason, your system	supports a more	advanced method	of SPS operation
    when installed on the Olivetti CP486 and when acting as a file-server
    in a multiuser  environment.  This allows automatic	``graceful'' shut-
    downs to be	performed under	operating-system control, without the need
    for	system administrator intervention. This	feature	is currently sup-
    ported by the latest version of SCO	UNIX System V/386 as described in
    the	following procedure:

      1.  A loss of external power of less than	20 seconds has no immedi-
	  ate effect on	the system; the	SPS switches in	to supply system
	  power	and the	LCD panel displays:


	       STANDBY POWER ON


	  If external power is restored	in that	time, the system switches
	  back to external power and the message returns to the	default
	  message (usually SYSTEM ACTIVE ).

      2.  If external power is still absent after 20 seconds, the UNIX
	  System starts	a graceful shutdown procedure, called a	``power-
	  fail process,'' and the LCD panel displays alternately:

	       SHUTDOWN	IN PROGRESS

	  and

	       STANDBY




    15 December	1990		    - 7	 -  The	Santa Cruz Operation, Inc.


    Release Notes

      3.  The powerfail	process	records	the information	necessary to res-
	  tart the system at the next power-up and broadcasts a	warning
	  message to all users of the system (terminals	in remote loca-
	  tions	might not be directly affected by the power outage).  UNIX
	  processes are	forewarned and terminated 40 seconds later, and
	  the powerfail	process	logs the event and finishes with a call	to
	  the system console for a conditional power-down.

      4.  A conditional	power-down means that:

	     o If external power was not restored, the console switches
	       off the system.

	     o If external power is restored, but the SPS battery voltage
	       is too low, then	the console still switches off the system.

	     o If external power is restored and the SPS batteries contain
	       sufficient charge to support another outage, then the sys-
	       tem resets and does not power down.

      5.  The front panel stays	on even	after the computer has been shut
	  down.	 The LCD panel displays:

	       PROG SHUTDOWN


      6.  When power is	restored after the system has been switched off,
	  the system reboots automatically.

































    15 December	1990		    - 8	 -  The	Santa Cruz Operation, Inc.







    ESC	Host Adapter Supplement

    Release and	Installation Notes

    Version 1.2.0


    1. Preface	1

    2. Configuration Requirements  1
    3. Installing the ESC Host Adapter Supplement  2

    4. Installation Order with Open Desktop 1.0	and UFE	 4
    5. Testing the Installation	 5

    6. Notes  5
       6.1 WARNING: Accessing Raw Devices on an	ODT 1.0.0 and Update E
	   System  5
       6.2 Reinstalling	the Link Kit  5
       6.3 Relinking the Kernel	 6
       6.4 Extended Memory Support  6
       6.5 Tape	Drive Accessing	Delay  6
    7. Selecting Boot and Root Devices	6

    8. Advanced	SPS Operation  7

































    15 December	1990		    - i	 -  The	Santa Cruz Operation, Inc.