TAPE(C)			      UNIX System V


	 Name
	      tape, mcart - magnetic tape maintenance program


	 Syntax
	      tape [ -csf8i ] [	-a arg ] command [ device ]

	      mcart command [ device ]


	 Description
	      tape sends commands to and receives  status  from	 the  tape
	      subsystem.   tape	can communicate	with QIC-02 cartridge tape
	      drives, SCSI tape	 drives,  and  QIC-40,	QIC-80	and  Irwin
	      mini-cartridge   tape   drives.	 (The	mcart  program	is
	      automatically invoked by tape when options specific  to  the
	      Irwin driver are used.)

	      tape reads /etc/default/tape to find the default device name
	      for sending commands and receiving status.  For example, the
	      following	line  in  /etc/default/tape  will  cause  tape	to
	      communicate with the QIC-02 cartridge tape device:

		   device = /dev/xct0

	      If a device name	is  specified  on  the	command	 line,	it
	      overrides	 the  default  device.	tape queries the device	to
	      determine	its device type.  If the device	does  not  respond
	      to  the  query, tape will	print a	warning	message	and assume
	      the device is a QIC-02 cartridge tape.

	      The   Irwin   driver   has   a	special	   default    file
	      /etc/default/mcconfig  that  contains special driver options
	      (see mcconfig(F)	for  details).	 In  addition,	the  Irwin
	      driver  uses  a  daemon  startup	program, /etc/mcdaemon,	to
	      provide background ECC encode/decode.

	      All driver messages are documented in the	messages(M) manual
	      page.


	 Options
	      You can explicitly specify the type of the device	 by  using
	      the device type flags, as	follows:

		   -c	QIC-02 cartridge tape
		   -s	SCSI tape
		   -f	QIC-40 mini-cartridge tape
		   -8	QIC-80 mini-cartridge tape
		   -i	Irwin mini-cartridge tape

	      The -a flag allows you to	pass an	argument to commands  that
	      can  use	them.  The format and setblk commands are the only
	      command that currently  can  take	 an  argument.	 A  format
	      argument	is  only valid with QIC-40 and QIC-80 tape drives,
	      and a setblk argument is only valid with SCSI drives.

	      The following commands can be used  with	the  various  tape
	      drivers  supported  under	 UNIX.	The letters following each
	      description indicate which drivers support each command:

		   A	All drivers
		   C	QIC-02 cartridge tape driver
		   S	SCSI tape driver
		   F	QIC-40 and QIC-80 mini-cartridge tape drivers
		   I	Irwin mini-cartridge tape driver

	      amount
	      Report amount of data in current or last transfer.  (C,S,F)

	      erase
	      Erase and	retension the tape cartridge.  (C,S,F)

	      load
	      Loads the	tape cartridge.	 (S)

	      reset
	      Reset  tape  controller  and  tape   drive.   Clears   error
	      conditions  and  returns	tape  subsystem	to power-up state.
	      (C,S,F)

	      reten
	      Retension	tape cartridge.	 Should	be  used  periodically	to
	      remedy  slack  tape  problems.   Tape  slack  can	 cause	an
	      unusually	large number of	tape errors.  (A)

	      rewind
	      Rewind to	beginning of tape.  (A)

	      status
	      The status output	looks like this:

		  status:   status message
		  soft errors:	 n
		  underruns:	 m

	      status message is	a report of  the  current  status  of  the
	      drive; ``no cartridge,'' ``write protected,'' or ``beginning
	      of tape''	are typical status messages.

	      soft  errors  is	the  number  of	 recoverable  errors  that
	      occurred	during	the  last  tape	 operation.  A recoverable
	      error  is	 one  which  is	 correctable  by  the	drive	or
	      controller.   An example of a non-recoverable ``hard'' error
	      is an attempt to write to	a write-protected cartridge.  Note
	      that  if	the  number  of	 soft  errors  greatly exceeds the
	      manufacturer's specifications, the drive may require service
	      or replacement.

	      underruns	is the number of times the tape	drive had to  stop
	      and  restart  due	 to tape buffer	underflows.  Underruns are
	      not an error indication, but that	the data transfer did  not
	      occur at the drive's maximum data	transfer rate.	The number
	      of underruns can be affected by system load.  (C,S,F)

	      unload
	      Unloads the tape cartridge.  (S)

	      format
	      Format the tape cartridge.   Floppy  controller-based  tapes
	      must  be	formatted  before  they	can be used.  This command
	      takes  approximately  one	 minute	 per  megabyte	 of   tape
	      capacity.	  If an	argument is provided with the -a flag, the
	      number  of  tracks  specified  by	 the  argument	 will	be
	      formatted.   Only	 even  numbers	less  than or equal to the
	      number of	tracks on the tape are allowed.	 (See tape(HW) for
	      more information.)  If no	argument is given, the entire tape
	      will be formatted.  (F,I)

	      getbb
	      Prints a list of bad tape	blocks detected	 during	 the  last
	      tape operation.  This listing can	be saved in a file for use
	      by the putbb command.  (F)

	      map
	      Prints out a map of the bad blocks on the	tape.  The  format
	      is a series of lines of the format:

	      track n: -------------X------...

	      Each '-' represents a  good  block  on  the  track;  an  'X'
	      represents a block marked	as bad.	 (F)

	      putbb
	      Reads a list of bad tape blocks from the standard	input  and
	      adds  them  to  the bad block table on the tape.	The format
	      expected by putbb	is the same  as	 generated  by	the  getbb
	      command.	(F)

	      rfm
	      Wind tape	forward	to the next file mark.	(C,S)

	      wfm
	      Write a file mark	at the current tape position.  (C,S)

	      setblk
	      Set the tape block size to a specified byte size	(S).   For
	      example,	the  following command sets the	tape block size	to
	      512 Bytes:
	      tape -a 512 setblk


	 Irwin-specific	Commands
	      The following commands are all specific to Irwin drives.

	      drive
		   displays information	about the  Irwin  driver  and  the
		   tape	drive.	An example display is:

		       Special file: /dev/rctmini
		       Driver version: 1.0.6a
		       Drive type: 285XL
		       Drive firmware: A0
		       Controller type:	SYSFDC
		       Unit select (0-3): 3

		   Special file	is the name of the special  file  used	to
		   access the driver.

		   Driver version is the version of the	driver linked with
		   the kernel.

		   Drive type is an ``equivalent'' tape	drive model number
		   as  determined by the MC driver.  Since the exact model
		   number of the tape drive depends on	the  drive's  form
		   factor  and	whether	 the  drive  is	mounted	in its own
		   cabinet, the	equivalent model number	 may  not  be  the
		   exact  model	of the installed tape drive. The following
		   is a	list of	equivalent drives:

		       110:	 110, 310, 410
		       120[XL]:	 120, 220, 320,	420, 720, 2020
		       125:	 125, 225, 325,	425, 725
		       145[XL]:	 145, 245, 345,	445, 745, 2040
		       165:	 165, 265, 465,	765
		       285XL:	 285, 485, 785,	2080
		       287XL:	 287, 487, 787,	2120

		   The brackets	 in  the  120[XL]  and	145[XL]	 mean  the
		   letters  ``XL''  may	 or  may not be	present.  When the
		   letters ``XL'' appear, the drive is	capable	 of  servo
		   writing extra long (i.e., 307.5 foot	DC2120)	tapes.

		   Note:  When this field displays ``125/145,''	 either	 a
		   125	drive or an early model	145 drive with a DC1000	is
		   present, the	driver can't distinguish between the  two.
		   A  125  drive  will	only  accept a DC1000 cartridge	(a
		   DC2000 or DC2120 will  not  fit).   A  145  drive  will
		   accommodate DC1000, DC2000, or DC2120 cartridges.

		   Drive firmware is the firmware part number and revision
		   level.   This  line	is  present  only for drives which
		   report this information.

		   Controller  type:  is  a  mnemonic	for   the   floppy
		   controller to which the tape	drive is attached:

		      Mnemonic	 Description
		      _________________________________________________
		      SYSFDC	 System	floppy controller
		      ALTFDC	 Alternate floppy controller
		      4100MC	 Irwin 4100MC Micro Channel controller
		      4100MCB	 Second	4100MC Micro Channel controller
		      4100	 Irwin 4100 PC Bus controller
		      4100B	 Second	4100 PC	Bus controller

		   Unit	select (0-3) gives the controller's  unit  select,
		   in  the range 0 through 3.  The unit	select selects the
		   drive.

	      info displays Irwin cartridge information.  For example:

		   Cartridge state: Formatted
		   Cartridge format: 145
		   Write protect slider	position: RECORD

		   Cartridge state is the current state	of the cartridge's
		   format.

		   Cartridge  format   indicates   the	 format	  on   the
		   cartridge's	tape.  The format is given in a	code which
		   is the same as the drive model on which  the	 cartridge
		   was	originally  formatted  (see drive and tape(HW) for
		   details). When the cartridge	is blank, the code has the
		   format which	would be applied by the	format command.

		   Write protect slider	position is RECORD or PROTECT.

	      capacity
		   cartridge capacity in 512-byte blocks.

	      kapacity
		   cartridge capacity in 1024-byte blocks.

		   These two commands give the total usable  data  storage
		   capacity  of	a formatted tape cartridge.  Variations	in
		   cartridge capacity are due to differing numbers of  bad
		   blocks.


	 Files
	      Devices:

	      /dev/rStp0    /dev/rct0	 /dev/erct0	/dev/rmc1
	      /dev/nrStp0   /dev/nrct0	 /dev/xct0	/dev/mcdaemon
	      /dev/xStp0    /dev/rct2	 /dev/rctmini
	      /dev/rft0	    /dev/nrct2	 /dev/xctmini
	      /dev/xft0	    /dev/xct0	 /dev/rmc0

	      /etc/default/tape	/etc/default/mcconfig /etc/mcdaemon

	      Include files:

	      /usr/include/sys/tape.h
	      /usr/include/sys/ct.h
	      /usr/include/sys/ft.h
	      /usr/include/sys/ir.h


	 See Also
	      backup(ADM), cpio(C), dd(C), restore(ADM), tape(HW), tar(C),
	      xbackup(ADM), xrestore(ADM) mcconfig(F) messages(M)


	 Notes
	      See tape(HW) for a list of supported tape	drives.

	      The amount and reset commands can	be used	while the tape	is
	      busy  with  other	operations.  All other commands	wait until
	      the currently executing command has  been	 completed  before
	      proceeding.

	      When you are using the non-rewinding tape	device or the tape
	      commands	rfm and	wfm, the tape drive light remains on after
	      the  command  has	 been  completed,  indicating  that   more
	      operations  may  be  performed on	the tape.  The tape rewind
	      command may be used to clear this	condition.

	      For more information on devicefiles, (listed above), see the
	      tape(HW) manual page.





	 TAPE(HW)			      UNIX System V


	 Name
	      tape - magnetic tape device

	 Description
	      The tape device implements the UNIX interface  with  a  tape
	      drive.  QIC-02 cartridge tape drives are supported by the	ct
	      device driver, QIC-40 and	QIC-80 tape  drives  connected	to
	      the  floppy disk controller are supported	with the ft device
	      driver, and Irwin	tape drives connected to the  floppy  disk
	      controller   are	 supported  with  the  mc  device  driver.
	      Typically,  the	tar(C),	  cpio(C),   dd(C),   backup(ADM),
	      xbackup(ADM),  xrestore(ADM),  or	 restore(ADM) commands are
	      used to access a tape drive.

	      A	single tape drive with	a  raw	(character,  non-blocking)
	      interface	 is  supported,	 except	 for  the SCSI tape driver
	      which supports up	to four	devices.  There	are four  standard
	      tape  device types. Devices beginning with the ``r'' prefix,
	      (for ``raw device''), should be used for	most  normal  tape
	      work,  while devices with	the ``n'' prefix, (``for no rewind
	      on  hold''),  should  be	used  for  storing  and	 restoring
	      multiple files.  Devices beginning with the ``x''	prefix are
	      control  devices,	 which	are  used  for	sending	  ioctl(S)
	      commands	to the tape subsystem.	Devices	beginning with the
	      ``e'' prefix (for	ECC device) support a 2/64 error  recovery
	      scheme.  Thus two	512-byte blocks	out of every 64	blocks can
	      be bad  and  the	driver	will  correct  the  errors.   This
	      software	ECC  support  provides	a  high	 degree	 of  error
	      recovery.

	      ECC encoding and decoding	for the	 ft  and  mc  floppy  tape
	      drivers  is  automatically  used	with  the  standard  ``r''
	      device; the ft and mc drivers do not support  the	 ``n''	or
	      ``e''  device  types.   On the QIC-40, QIC-80 and	Irwin 80MB
	      drives, for every	29K written to the tape, 3K of ECC data	is
	      written with it to provide error recovery.  On the Irwin 10,
	      20, 40 and 60MB drives, for every	16K written to	the  tape,
	      2K of ECC	data is	written.

	      QIC-40 and QIC-80	tapes must be formatted	with  the  tape(C)
	      command  before  use,  unless  you use QIC-40 or QIC-80 pre-
	      formatted	tapes, respectively.  Similarly, Irwin tapes  must
	      be  first	 servo-written	and  then  formatted  with tape(C)
	      before use, unless you use Irwin pre-formatted  tapes.   The
	      mc  driver  can read tapes formatted and written under XENIX
	      but cannot write to them.

	      The following table summarizes the base  naming  conventions
	      for the tape drives supported:

		   ct0,1	  QIC24	unit 0,1
		   ct2,3	  QIC11	unit 0,1
		   Stp0,1,2,3	  SCSI tape unit 0,1,2,3
		   ft0		  QIC-40 or QIC-80 floppy tape unit
		   mc0		  Irwin	floppy tape unit
		   ctmini	  default mini-cartridge device
		   mt0,1	  reel to reel unit 0,1	1600 bpi
		   mt2,3	  reel to reel unit 0,1	800 bpi
		   mt4,5	  reel to reel unit 0,1	6250 bpi

	      The  default   tape   device   is	  stored   in	the   file
	      /etc/default/tape,   which   is	also   used   by  tape(C).
	      /etc/default/tape	should always contain the ``x''	 (control)
	      device  name  of the default device, and is normally updated
	      by mkdev(ADM) tape.  If the default  device  is  an  QIC-40,
	      QIC-80  or Irwin tape drive, the appropriate device from the
	      table above will be linked to the	ctmini device node.   QIC-
	      02  tape	drives will always be accessed by the ct0,1 device
	      nodes as shown in	the  table.   If  a  SCSI  tape	 drive	is
	      installed	as the default device and there	is no QIC-02 drive
	      installed, it will be linked to the  ct0	device	node.	If
	      both  SCSI  and QIC-02 drives are	installed, the SCSI device
	      node cannot be linked to the ct0 device node.

	      tape(C) describes	the commands used to access tape drives.


	 Definition of ioctl commands
	      The following ioctl commands can be used	with  the  various
	      tape  device  drivers  supported	under  UNIX.   The letters
	      following	each description indicate  which  drivers  support
	      each ioctl command:

		   A	All drivers
		   C	QIC-02 cartridge tape driver
		   S	SCSI tape driver
		   F	QIC-40 and QIC-80 mini-cartridge tape drivers
		   I	Irwin mini-cartridge tape driver


	      MT_STATUS
	      Returns a	device-independent structure holding the status	of
	      the   drive.    The   tape_info	structure  is  defined	in
	      /usr/include/sys/tape.h.	(C,S,F)

	      MT_DSTATUS
	      Returns  a   device-dependent   structure	  holding   status
	      information of the drive.	 (C,S,F)

	      MT_RESET
	      Resets the driver	software and the tape  drive.	Interrupts
	      tape commands in progress.  (C,S,F)

	      MT_REPORT
	      Returns an integer code which determines the type	of  device
	      which  the driver	controls.  The type numbers are	defined	in
	      /usr/include/sys/tape.h.	(C,S,F)

	      MT_RETEN
	      Winds the	tape forward to	EOT  and  then	backward  to  BOT.
	      (C,S,F)

	      MT_REWIND
	      Rewinds the tape to BOT.	(C,S,F)

	      MT_ERASE
	      Erases the data on the tape and  retensions  the	cartridge.
	      (C,S,F)

	      MT_AMOUNT
	      Returns an integer count of the  amount  of  the	last  data
	      transfer.	 (C,S,F)

	      MT_FORMAT
	      Formats the tape.	 Expects as  an	 argument  the	number	of
	      tracks  to  format,  which  must	be  an even number.  If	no
	      argument is provided, the	default	is 20  tracks  for  QIC-40
	      drives, and 28 tracks for	QIC-80 drives.	(F)

	      MT_GETHDR
	      Expects as an argument a pointer to a  struct  ft_header	or
	      struct  ir_header	 and copies the	header of the current tape
	      into it.	(F)

	      MT_PUTHDR
	      Takes a pointer to a struct ft_header  or	 struct	 ir_header
	      and  writes  it  onto the	tape.  This command should be used
	      with caution.  (F)

	      MT_GETNEWBB
	      Takes a pointer to a struct ft_newbbt  or	 struct	 ir_newbbt
	      and  copies  in  a  list	of bad blocks detected on the last
	      write operation.	(F)

	      MT_PUTNEWBB
	      Takes a pointer to a struct ft_newbbt or	struct	ir_newbbt,
	      reads  in	 the  header  from the tape, then writes a new bad
	      block onto the  tape  with  the  new  bad	 blocks	 from  the
	      provided bad block table.	 (F)

	      MT_SETBLK
	      Sets the block size (in bytes) of	the tape blocks.  Takes	as
	      an argument the size in bytes. (S)

	      MT_GETVTBL
	      Takes a pointer to a struct ft_vtbl and copies in	the volume
	      table from the tape.  (F)

	      MT_PUTVTBL
	      Takes a pointer to a struct ft_vtbl and  writes  the  volume
	      table  onto  the	tape.	This  command  should be used with
	      caution.	(F)

	      MT_RFM
	      Winds the	tape forward to	the next file mark.  (C,S)

	      MT_WFM
	      Writes a file mark at the	 current  location  on	the  tape.
	      (C,S)

	      MT_LOAD
	      On devices which are capable of doing  so,  loads	 the  tape
	      into the drive.  (S)

	      MT_UNLOAD
	      On devices which are capable of doing so,	unloads	 the  tape
	      from the drive.  (S)


	 Irwin-specific	ioctl Interface
	      Device specific  functions  of  the  Irwin  tape	drive  are
	      accessed	via  special  commands	passed to the Irwin driver
	      using the	ioctl()	 interface.   An  Irwin	 driver	 interface
	      library  is  available.	This  library  provides	 a  system
	      independent  interface  to  ioctl()  via	the  entry   point
	      mcioctl():

	      #include "mc.h"

	      int mcioctl(fh, cmd, arg)
	      int fh;	     /*	File handle from open()	*/
	      int cmd;	     /*	MCCTL_*	command	code */
	      void *arg;     /*	Additional argument pointer */

	      mcioctl(fh, MCCTL_NOP, NULL)
	      mcioctl(fh, MCCTL_VERSION, verbuf)
	      mcioctl(fh, MCCTL_CAPACITY, capp)
	      mcioctl(fh, MCCTL_LSEEK, lskbuf);
	      mcioctl(fh, MCCTL_REWIND)
	      mcioctl(fh, MCCTL_RETEN)
	      mcioctl(fh, MCCTL_REWIND_NW)
	      mcioctl(fh, MCCTL_RETEN_NW)
	      mcioctl(fh, MCCTL_GETDRVCFG, cfgbuf)
	      mcioctl(fh, MCCTL_GETCFG,	cfgbuf)
	      mcioctl(fh, MCCTL_SETCFG,	cfgbuf)
	      mcioctl(fh, MCCTL_GETTHDR, hdrbuf)
	      mcioctl(fh, MCCTL_PUTTHDR, hdrbuf)
	      mcioctl(fh, MCCTL_GETDLISTS, listbuf)
	      mcioctl(fh, MCCTL_FLUSH)
	      mcioctl(fh, MCCTL_FORMAT,	fmtbuf)
	      mcioctl(fh, MCCTL_FMTSTAT, fmtbuf)
	      mcioctl(fh, MCCTL_ABORT)
	      mcioctl(fh, MCCTL_DEVSTAT, dstatp)
	      mcioctl(fh, MCCTL_GETERCTL, erctlp)
	      mcioctl(fh, MCCTL_SETERCTL, erctlp)
	      mcioctl(fh, MCCTL_GETER, ierrp)
	      struct mcver *verbuf;    /* version buffer */
	      long *capp;	       /* capacity in bytes */
	      struct mclseek *lskbuf;  /* tape logical position	descriptor */
	      struct mccfg *cfgbuf;    /* configuration	buffer */
	      char *hdrbuf;	       /* 1024 byte header buffer */
	      unsigned short * listbuf;	/* 2048	byte defect list buffer	*/
	      struct mcfmt *fmtbuf;    /* format control/status	buffer */
	      unsigned short *dstatp;  /* device status	word */
	      unsigned short *erctlp;  /* error	control	word */
	      unsigned short *ierrp;   /* device specific error	*/

	      mcioctl()	provides system	independent ioctl interface to the
	      Irwin driver.  This subroutine is	essentially a pass-trough.
	      That is, arguments are passed  through  to  ioctl().   If	 a
	      device  specific	error occurs (i.e., a non-system error)	at
	      completion of the	system ioctl() and the	command	 is  other
	      than   MCCTL_NOP	 or   MCCTL_VERSION,   mcioctl()  executes
	      ioctl(MCCTL_GETER) to retrieve the device	specific error.

	      The following ioctl commands are	available  for	the  Irwin
	      driver:

	      MCCTL_NOP
		   No operation.  The  argument	 is  ignored.	A  success
		   status is returned.	This command may be used as an aid
		   in determining if a	special	 file  refers  to  the	MC
		   driver.

	      MCCTL_VERSION
		   Gets	driver version information.  The argument  is  the
		   address of version information buffer (see struct mcver
		   in /usr/include/sys/mc.h) to	which the driver writes.

	      MCCTL_CAPACITY
		   Gets	a tape's capacity in bytes. The	 argument  is  the
		   address of a	long integer.

	      MCCTL_REWIND
	      MCCTL_RETEN
	      MCCTL_REWIND_NW
	      MCCTL_RETEN_NW
		   These four commands physically  position  the  tape	at
		   high	 speed.	  MCCTL_RETEN  and  MCCTL_RETEN_NW run the
		   tape	 to  the  early	 warning  hole	first.	 All  four
		   commands  return  the  tape	to  the	 load-point  hole.
		   MCCTL_REWIND_NW and MCCTL_RETEN_NW start a request  but
		   don't wait for completion.

	      MCCTL_GETDRVCFG
	      MCCTL_GETCFG
	      MCCTL_SETCFG
		   These three commands	provide	 access	 to  configuration
		   parameters for a particular a mini cartridge	tape unit.
		   The structure  of  these  parameters	 is  struct  mccfg
		   (defined  in	 /usr/include/sys/mc.h)	This structure has
		   driver, tape	drive, and cartridge related fields.  Both
		   MCCTL_GETDRVCFG  and	 MCCTL_GETCFG  copies the driver's
		   the MCCFG  structure	 to  the  caller's  buffer.   When
		   MCCTL_GETDRVCFG  is	used,  struct  mccfg  members with
		   driver and tape drive related fields	are returned.	No
		   error  is  given  when  a  cartridge	 is  absent.  When
		   MCCTL_GETCFG	 is  used  successfully,  all  fields  are
		   returned  with  valid data.	An error is returned if	no
		   cartridge is	present.  MCCTL_SETCFG allows  the  caller
		   to adjust certain fields in the driver's configuration.

	      MCCTL_GETTHDR
	      MCCTL_PUTTHDR
		   MCCTL_GETTHDR and MCCTL_PUTTHDR read	and write the 1024
		   byte	 tape header in	block 0.  MCCTL_PUTTHDR	assumes	an
		   Irwin style header.	The  the  following  procedure	is
		   used	to write the header:
		      Tape block 0 is read to a	buffer.	 The caller's 1024
		      byte  header  buffer  is copied to the first, fifth,
		      and when space permits,  the  ninth  and	thirteenth
		      1024-byte	sectors	in the buffer.	When the cartridge
		      format uses ECC  (i.e.,  other  than  110	 cartridge
		      format), the header's ECC	in use field is	set.  When
		      the cartridge format uses	ECC, ECC  is  encoded.	 A
		      check  sum is calculated for the buffer.	The buffer
		      is written back to block 0.  Block 0 is  reread  and
		      the cartridge state is redetermined.  A new checksum
		      is calculated and	compared against the original.

	      MCCTL_GETDLISTS
		   Returns lists used by  the  driver's	 flaw  management.
		   The	caller	gives  the address of a	buffer which is	at
		   least 2 KB in length.  Four lists  are  copied  to  the
		   buffer.   Each list is comprised of physical	tape block
		   numbers  stored  as	 unsigned   short   integers   and
		   terminated  with  the  value	 0xffff.   The	lists  are
		   contiguous and given	in the following order:
		       Primary Defect List (PDL)
		       Working Defect List (WDL)
		       Grown Defect List (GDL)
		       Relocation List (RL)

	      MCCTL_FLUSH
		   Flushes dirty  buffers  to  tape.   MCCTL_FLUSH  forces
		   dirty buffers in the	Irwin driver's cache to	be written
		   to tape.  The pointer  argument  is	ignored.   Control
		   returns    when   data   is	 written.    Buffers   are
		   automatically flushed upon a	close()	or when	the device
		   is  idle  for  a  certain  period  (see mc_autoflush	in
		   struct mccfg	in /usr/include/sys/mc.h).

	      MCCTL_FORMAT
	      MCCTL_FMTSTAT
		   MCCTL_FORMAT	 starts	 a  erase,   servo-format-certify-
		   initialize	header	 or  re-certify	 operations.   The
		   argument  is	 the  address	of   struct   mcfmt   (see
		   /usr/include/sys/mc.h).	 Formatting	operations
		   performed depend upon the  values  in  the  structure's
		   fm_cmd   and	  fm_option   fields,	and  struct  mccfg
		   mc_cartstate	 field.	  When	an  MCCTL_FORMAT   command
		   completes   successfully,   MCCTL_FMTSTAT  is  used	to
		   determine the progress (when	a no-wait flag is set)	or
		   results     of    formatting.     Like    MCCTL_FORMAT,
		   MCCTL_FMTSTAT also  uses  the  struct  mcfmt	 structure
		   (typically the same one passed to MCCTL_FORMAT).

	      MCCTL_ABORT
		   Used	to interrupt and terminate operations  started	by
		   MCCTL_FORMAT.  The pointer argument is ignored. Control
		   returns after formatting has	terminated.

	      MCCTL_DEVSTAT
		   Returns a 16-bit device  status  word  to  an  unsigned
		   short  integer  who's  address  is  passed in the third
		   argument of ioctl().	 This field is intended	for use	by
		   applications	 which	use  the tape drive interactively.
		   The status  bits  are  defined  in  struct  mclseek	in
		   /usr/include/sys/mc.h.

	      MCCTL_GETERCTL
	      MCCTL_SETERCTL
		   MCCTL_GETERCTL  and	MCCTL_SETERCTL	give   application
		   access  to  the state of and	control	over certain error
		   mechanisms.	The argument is	the address  of	 a  16-bit
		   error  control  variable  which the Irwin driver writes
		   with	current	values for MCCTL_GETERCTL  and	reads  for
		   MCCTL_SETERCTL.   Certain  flags may	or may not have	an
		   effect depending on the implementation. Bit values  for
		   the	  error	   control   variable	are   defined	in
		   /usr/include/sys/mc.h.

	      MCCTL_GETER
		   Gets	device specific	error: IE_*.  In general the value
		   0  is returned to indicate success or -1 to indicate	an
		   error.  When	mcioctl() returns the value -1,	 an  error
		   has	occurred.   The	 error	condition  may	have  been
		   detected in the operating system or in the driver.	In
		   order  to  discriminate  the	origin the global _mcerrno
		   should be examined first  (before  errno).	When  non-
		   zero, the error was returned	by the driver.	Values for
		   _mcerrno are	defined	in /usr/include/ierrno.h  with	an
		   IE_ prefix.


	 Floppy	Tape Drive Configuration and Media
	      This section is concerned	with QIC-40 and	QIC-80 tape drives
	      and supported floppy tape	cartridges.

	    Configuration Options for the Floppy Tape Driver (ft)
	      Five configuration options are available for the floppy tape
	      driver  (ft)  for	 QIC-40	 and QIC-80 tape drives.  To alter
	      these variables, it is necessary to edit	the  configuration
	      file  /etc/conf/pack.d/ft/space.c,  relink  the  kernel, and
	      reboot the system	with the new kernel.   While  all  options
	      may  be  edited  manually	 in  space.c, the first	and second
	      options -	ft_drivetype and ft _select_mode  -  may  also	be
	      modified	using  the mkdev(ADM) tape command.  These options
	      are summarized in	the following table:

	       __________________________________________________________
	       |	Floppy Tape Drive Configuration	Options		 |
	       |_________________________________________________________|
	       |Variable	| Values		|    Editing	 |
	       |		|			| mkdev	  Manual |
	       |________________|_______________________|_______|________|
	       |ft_drive_type	| FT_QIC40		|  yes	|  yes	 |
	       |		| FT_QIC40XL (FT_QIC60)	|	|	 |
	       |		| FT_QIC80		|	|	 |
	       |		| FT_QIC80XL		|	|	 |
	       |________________|_______________________|_______|________|
	       |ft_select_mode	| FT_HARD_SELECT	|  yes	|  yes	 |
	       |		| FT_SOFT_SELECT	|	|	 |
	       |________________|_______________________|_______|________|
	       |ft_alloc_switch	| FT_OPEN_TIME		|  no	|  yes	 |
	       |		| FT_INIT_TIME		|	|	 |
	       |________________|_______________________|_______|________|
	       |ft_minbufs	| 2 < x	< (ft_maxbufs)	|  no	|  yes	 |
	       |________________|_______________________|_______|________|
	       |ft_maxbufs	| (ft_minbufs) < x < 20	|  no	|  yes	 |
	       |________________|_______________________|_______|________|

	      ft_drivetype
		   When	set from FT_QIC40 to FT_QIC40XL, or from  FT_QIC80
		   to FT_QIC80XL, ft_drivetype enables support of extended
		   length (307.5 ft) DC2120 mini-cartridges in the driver.
		   FT_QIC60  is	 an  obsolete  value; FT_QIC40XL should	be
		   used	instead.

		   A  QIC-40  drive  should   never   be   operated   with
		   ft_drivetype	 set  to  FT_QIC80 or FT_QIC80XL.  Also, a
		   QIC-80 drive	should never be	operated with ft_drivetype
		   set	to  FT_QIC40  or  FT_QIC40XL.	If  they are, your
		   system may panic or hang, or	data may be lost from  the
		   tape	media

	      ft_select_mode
		   When	set to FT_HARD_SELECT, the  ft	driver	expects	 a
		   normal  tape	 drive	with  a	 drive select jumper to	be
		   present.  If	ft_select_mode is set  to  FT_SOFT_SELECT,
		   the	ft driver uses Soft Select mode	to access the tape
		   drive, which	must be	a  Soft	 Select-compatible  QIC-40
		   or  QIC-80  tape  drive  with  no  drive select jumpers
		   installed.

	      ft_alloc_switch
		   When	set  to	 FT_OPEN_TIME,	the  ft	 driver	 allocates
		   memory  when	 it is needed, and frees memory	once it	is
		   no longer needed.  Typically, memory	 is  allocated	at
		   open	  time	 and   released	  at   close  time.   When
		   ft_alloc_switch is  set  to	FT_INIT_TIME,  all  memory
		   allocation is done at init time (when the system boots)
		   and the ft driver retains this memory.   The	 advantage
		   of	init  time  allocation	is  that  more	memory	is
		   available for the ft	buffers.  The disadvantage is that
		   this	 memory	 is  held by the tape driver and cannot	be
		   used	elsewhere in the system.

	      ft_minbufs
	      ft_maxbufs
		   These variables set the minimum and maximum	number	of
		   32K	buffers	that the ft driver is allowed to use.  The
		   lower limit of the minimum is hard set to 2,	 with  any
		   value  lower	 than 2	interpreted as 2.  The upper limit
		   of the maximum is hard set to 20, with numbers  greater
		   than	  20  interpreted  as  20.   When  the	ft  driver
		   allocates memory for	buffers,  it  requests	ft_maxbufs
		   first.   If	this  fails, ft	reduces	its request by one
		   and	tries  again.  This  continues	until  either  the
		   request  is	satisfied or ft_minbufs	buffers	fail to	be
		   allocated.	If  the	 request  is  satisfied,  then	ft
		   proceeds.  Otherwise,  the  tape  operation	fails  and
		   ENOMEM (Error, no memory for	buffers) is returned.
		   The exception to this is when ft_alloc_switch is set	to
		   FT_INIT_TIME	 (allocation takes place at init time).	If
		   the ft_minbufs are not available at init time, then	ft
		   resorts  to allocation as needed (as	if ft_alloc_switch
		   were	set to FT_OPEN_TIME).  If this condition occurs, a
		   warning is printed at init time.

		   It is recommended that ft_minbufs be	set to at least	3.
		   Although  the driver	can operate with only two buffers,
		   performance	is  seriously  degraded;  the  tape  never
		   streams, and	in fact	produces an underrun for every 32K
		   block written to the	tape.

	    Floppy Tape	Cartridge Media
	      There are	three mini-cartridge types appropriate	to  floppy
	      tape drives:

			 ______________________________________
			 |  Floppy Tape	Mini-Cartridge Types   |
			 |_____________________________________|
			 |Cartridge | Length | Width | Maximum |
			 |	    |  (ft)  | (in)  | Density |
			 |	    |	     |	     | (ftpi)  |
			 |__________|________|_______|_________|
			 |DC2000    | 205    | 0.25  | 12,500  |
			 |DC2080    | 205    | 0.25  | 14,700  |
			 |DC2120    | 307.5  | 0.25  | 14,700  |
			 |__________|________|_______|_________|

	      DC2000 and DC2080	are available unformatted or  preformatted
	      from  the	manufacturer.  Irwin format tapes are incompatible
	      with the floppy tape driver.

	      If a 2120	cartridge is inserted into  a  drive,  it  can	be
	      detected	as  an	extended length	tape and will be formatted
	      for 60 Mbytes on QIC-40 drives, and  120	Mbytes	on  QIC-80
	      drives.  Some  older  QIC40  drives  are	not able to detect
	      extended	length	tapes.	 These	models	should	never	be
	      operated	with  a	 DC2120	inserted, since	they will expect a
	      205 foot tape length.   Drives  cannot  distinguish  between
	      blank  (unformatted)  DC2000  &  DC2080.	 Never	attempt	to
	      format a DC2080 in a QIC-40 drive, or a DC2000 in	 a  QIC-80
	      drive.

	      Media configurations for floppy tape drives  are	summarized
	      in the following table:

	       __________________________________________________________
	       |	 Floppy	Tape Drive Media Configurations		 |
	       |_________________________________________________________|
	       |Drive  | ft_drivetype |	Media	| Formatted | Operations |
	       |       |	      |		| Capacity  |		 |
	       |       |	      |		|    (MB)   |		 |
	       |_______|______________|_________|___________|____________|
	       |QIC-40 | FT_QIC40     |	DC2000	|    40	    |	r/w/f	 |
	       |_______|______________|_________|___________|____________|
	       |QIC-40 | FT_QIC40XL   |	DC2000	|    40	    |	r/w/f	 |
	       |       |	      |	DC2120	|    60	    |	r/w/f	 |
	       |_______|______________|_________|___________|____________|
	       |QIC-80 | FT_QIC80     |	DC2000	|    40	    |	  r	 |
	       |       |	      |	DC2080	|    80	    |	r/w/f	 |
	       |_______|______________|_________|___________|____________|
	       |QIC-80 | FT_QIC80XL   |	DC2000	|    40	    |	  r	 |
	       |       |	      |	DC2120	|    60	    |	  r	 |
	       |       |	      |	DC2080	|    80	    |	r/w/f	 |
	       |       |	      |	DC2120	|    120    |	r/w/f	 |
	       |_______|______________|_________|___________|____________|


	 Irwin Drive and Cartridge Models
	      This  section  is	 concerned  with  Irwin	 tape  drives  and
	      cartridges supported.

	    Drive Models
	      Many Irwin mini cartridge	drives have a  three  digit  model
	      number.  Each  digit  has	 a  meaning.  The high order digit
	      encodes the form factor and cabinetry:
	       1xx   5-1/4 inch	drive (mounted in system cabinet).
	       2xx   3-1/2 inch	drive (mounted in system cabinet).
	       3xx   5-1/4 inch	drive in a metal cabinet w/ power supply.
	       4xx   3-1/2 inch	drive in a plastic cabinet (no supply).
	       7xx   3-1/2 inch	drive in a metal cabinet w/ power supply.

	      The middle digit	gives  the  approximate	 capacity,  in	10
	      Megabyte	units  for  a  standard	 capacity (not extra long)
	      tape:

				   x1x	 10 Megabytes
				   x2x	 20
				   x4x	 40
				   x6x	 60
				   x8x	 80

	      The low digit encodes the	drive's	normal data transfer  rate
	      (i.e., the floppy	controller data	clock rate).

			       xx0   250 Kilobits/Second
			       xx5   500 Kilobits/Second
			       xx7   1 Megabit/Second

	      In addition, a new 4-digit model numbering system	is in use.
	      These  model  numbers  are  associated with drives which are
	      adaptable	to different  system  hardware	environments  with
	      accessory	hardware kits.

		2020   3-1/2 inch, 20 Megabyte,	250 Kilobits/Second
		2040   3-1/2 inch, 40 Megabyte,	500 Kilobits/Second
		2080   3-1/2 inch, 80/120 Megabyte, 500	Kilobits/Second
		2120   3-1/2 inch, 80/120 Megabyte, 1 Megabit/Second

	    Mini Cartridges
	      There are	three primary physical mini cartridges types:

	       DC1000	185 feet of 0.150 inch wide tape (same as TC-200)
	       DC2000	205 feet of 0.250 inch wide tape (same as TC-400)
	       DC2120	307.5 feet of 0.250 inch wide tape

	      The DC1000 cartridge is physically thinner than  DC2000  and
	      DC2120  cartridges.   The	 DC2000	 and  DC2120 have the same
	      physical form but	the  DC2120  has  a  longer  tape.   These
	      cartridges are distinguished by their labels.  Each physical
	      cartridge	type has at least two cartridge	formats:


 ___________________________________________________________________________
|		       Mini (Irwin) Cartridge Format Parameters             |
|___________________________________________________________________________|
|	| AccuTrak |	    |	     |	    |	     |  Sectors	  |         |
|Cart-  | Reorder  | Cart-  | Total  |	    | Blocks |	per	  |         |
|ridge  | Number   | ridge  | Tape   | Trks | per    |   Block	  | Density |
|Format | see note |	    | Blocks |	    | Track  | Data   ECC | (ftpi)  |
|_______|__________|________|________|______|________|______|_____|_________|
|110    | 1000-10  | DC1000 | 1264   | 8    | 158    | 8    | 0	  | 6400    |
|120    | 2000-20  | DC2000 | 1190   | 14   | 85     | 16   | 2	  | 6400    |
|120XL  | 2000-30  | DC2120 | 1792   | 14   | 12     | 16   | 2	  | 6400    |
|125    | 1000-20  | DC1000 | 1320   | 12   | 110    | 16   | 2	  | 10000   |
|145    | 2000-40  | DC2000 | 2480   | 20   | 124    | 16   | 2	  | 10000   |
|145XL  | 2000-60  | DC2120 | 3720   | 20   | 186    | 16   | 2	  | 10000   |
|165    | 2000-64  | DC2000 | 3936   | 24   | 164    | 16   | 2	  | 13200   |
|285    | 2000-80  | DC2000 | 2752   | 32   | 86     | 29   | 3	  | 11600   |
|285XL  | 2000-120 | DC2120 | 4160   | 32   | 130    | 29   | 3	  | 11600   |
|_______|__________|________|________|______|________|______|_____|_________|

		   Notes:    The  suffix  part	of  the	 AccuTrak  Reorder
			     Number  is	 an approximate	cartridge capacity
			     in	Megabytes.

			    All	formats	use 1024 byte MFM encoded sectors.

	  _________________________________________________________________
	  |  Drive Read/Write	Compatibility for Mini Cartridge Formats   |
	  |________________________________________________________________|
	  |			Drive Model (See Note) 			   |
	  |________________________________________________________________|
	  |	  |	| 2020   |     | 2040 |	    |	   |	  | 	   |
	  |	  |	| 720	 | 725 | 745  |	    |	   |	  | 	   |
	  |	  |	| 420	 | 425 | 445  |	765 | 2080 | 2120 | 	   |
	  |Cart-  | 410 | 320	 | 325 | 345  |	465 | 785  | 787  | 	   |
	  |ridge  | 310 | 220	 | 225 | 245  |	265 | 485  | 487  | Cart-  |
	  |Format | 110 | 120	 | 125 | 145  |	165 | 285  | 287  | ridge  |
	  |_______|_____|________|_____|______|_____|______|______|________|
	  |110    | rw  | rw	 | r-  | r-   |	r-  | r-   | r-	  | DC1000 |
	  |120    | --  | rw	 | --  | r-   |	r-  | r-   | r-	  | DC2000 |
	  |120XL  | --  | rw	 | --  | r-   |	r-  | r-   | r-	  | DC2120 |
	  |125    | --  | --	 | rw  | rw   |	r-  | r-   | r-	  | DC1000 |
	  |145    | --  | --	 | --  | rw   |	r-  | r-   | r-	  | DC2000 |
	  |145XL  | --  | --	 | --  | rw   |	r-  | r-   | r-	  | DC2120 |
	  |165    | --  | --	 | --  | --   |	rw  | r-   | r-	  | DC2000 |
	  |285    | --  | --	 | --  | --   |	--  | rw   | rw	  | DC2000 |
	  |285XL  | --  | --	 | --  | --   |	--  | rw   | rw	  | DC2120 |
	  |_______|_____|________|_____|______|_____|______|______|________|

		  Key:

		       r     Drive reads cartridge format

		       w     Drive writes cartridge format

		       -     Incompatible: When	a cartridge  is	 formatted
			     but  incompatible for reading or writing, the
			     driver reports that the cartridge	is  either
			     incompatible or erased.

	    Extra Long (XL) DC2120 Cartridge Compatibility
	      Extra long (i.e.,	DC2120)	cartridges are	incompatible  with
	      the  following  drives  as  the  drive  will  not	physically
	      accommodate the cartridge:

	      110, 310,	410, 125, 225, 325, 425, and 725

	      Even though DC2120 cartridges are	physically accepted in the
	      following	drives,	they may not be	formattable:

	      120, 220,	320, 420, 720, 2020, 145, 245, 345, 445, 745, 2040

	      Drives manufactured previous to about 1989  don't	 recognize
	      the longer tape.	However, the MC	driver is able to read and
	      write preformated	extra long tapes in these drives,  but	it
	      is  unable to correctly format them.  Formatting will start,
	      but terminate  in	 error.	  To  determine	 whether  a  drive
	      supports	formatting  of	DC2120	cartridges,  use the mcart
	      utility.	If the command mcart drive reports  a  drive  type
	      with  the	 suffix	 XL,  formatting  of  DC2120 cartridges	is
	      supported.


	 Files
	      /dev/rStp0    /dev/rct0	 /dev/erct0	/dev/rmc1
	      /dev/nrStp0   /dev/nrct0	 /dev/xct0	/dev/mcdaemon
	      /dev/xStp0    /dev/rct2	 /dev/rctmini
	      /dev/rft0	    /dev/nrct2	 /dev/xctmini
	      /dev/xft0	    /dev/xct0	 /dev/rmc0

	      Include files:

	      /usr/include/sys/tape.h
	      /usr/include/sys/ct.h
	      /usr/include/sys/ft.h
	      /usr/include/sys/ir.h
	      /usr/include/sys/mc.h
	      /usr/include/sys/mcheader.h


	 Notes
	      After certain  tape  operations  are  executed,  the  system
	      returns a	prompt before the tape controller has finished its
	      operation.  If the user  enters  another	tape  command  too
	      quickly,	a ``device busy'' error	is returned until the tape
	      device is	finished with its previous operation.

	      Periodic tape cartridge retensioning and tape head  cleaning
	      are necessary for	continued error-free operation of the tape
	      subsystem.  Use tape(C) to retension the tape.


	 See Also
	      backup(ADM),  xbackup(ADM),   cpio(C),   dd(C),	format(C),
	      mkdev(ADM), tape(C), tar(C), restore(ADM), xrestore(ADM)


							     TAPE(HW)






	 MKDEV(ADM)			      UNIX System V


	 Name
	      mkdev - calls scripts to add peripheral devices


	 Syntax
	      /etc/mkdev dos
	      /etc/mkdev fd
	      /etc/mkdev fs [ device file ]
	      /etc/mkdev hd [ [	disk ] [ controller| adapter ] ] [ lun ]
	      /etc/mkdev mouse
	      /etc/mkdev serial
	      /etc/mkdev shl
	      /etc/mkdev streams
	      /etc/mkdev tape


	 Description
	      mkdev  creates  the  device  file(s)   associated	  with	 a
	      peripheral  device.   Based  on  the  argument supplied, the
	      mkdev  command  calls  a	script	found  in  the	 directory
	      /usr/lib/mkdev.	 (There	 may  be  scripts  found  in  this
	      directory	that  are  specific  to	 a  given  application	or
	      software	package	 that  are  not	 documented  here.)  If	no
	      arguments	are listed, mkdev prints a usage message.

	      /etc/mkdev dos initializes necessary devices and	configures
	      the system to support mounted DOS	filesystems.

	      /etc/mkdev hd creates device files for use with a	peripheral
	      hard  disk.  The	device	files  for  an	internal hard disk
	      already	exist.	  invokes   the	   following	utilities:
	      dparam(ADM), badtrk(ADM),	fdisk(ADM), and	divvy(ADM).  mkdev
	      hd  includes  an	extended  syntax  for  use   on	  multiple
	      controllers.   These  syntax extensions use numbers to refer
	      to the disk and controller numbers.

	      In addition, the codes ST506-, OMTI-, and	SCSI- can be  used
	      to  refer	 to the	controller/adapter number, as shown in the
	      tables below.

	      ST506 disks will install with one	of the following commands:

	      mkdev hd 0 0 (or ST506-0)	    first disk on first	controller
	      mkdev hd 1 0 (or ST506-0)	    second disk	on first controller
	      mkdev hd 0 1 (or ST506-1)	    first disk on second controller
	      mkdev hd 1 1 (or ST506-1)	    second disk	on second controller

	      ESDI disks will install with one of the following	commands:

	      mkdev hd 0 0 (or OMTI-0) first disk on controller	(root disk)
	      mkdev hd 1 0 (or OMTI-0) second disk on controller

	      SCSI disks require three pieces of  information:	the  drive
	      number,  the  adapter  number,  and  the	lun  (logical unit
	      number).	 SCSI  disks  will  install  with  the	 following
	      command:

	              mkdev hd [0-7] [SCSI-0 or	SCSI-1]	[0-7]

	      mkdev hd must be invoked twice to	install	a SCSI disk.   The
	      first  time,  the	kernel will be reconfigured to support the
	      new disk.	 The second time, the disk  will  be  initialized.
	      Use the same mkdev hd arguments both times.

	      /etc/mkdev serial	creates	device files for use  with  serial
	      cards.  The  device  files  for  the  first and second ports
	      already exist.  Additional device	files must be created  for
	      the  ports  added	 when  expansion  cards	 are  added to the
	      system.

	      /etc/mkdev  streams  configures  the  kernel   for   streams
	      support.

	      /etc/mkdev fs performs the system	maintenance tasks required
	      to  add  a  new  filesystem to the system	once the device	is
	      created (mknod(C)) and the filesystem is	made  (mkfs(ADM)).
	      It  creates  the	/file  and   /file/lost+found directories,
	      reserves slots  in  the  lost+found  directory,  (if  either
	      already  exist,  they  are  used	unmodified)  and  modifies
	      /etc/checklist,  /etc/default/filesys  and  /etc/default	to
	      check  (fsck(ADM)) and mount (mount(ADM),	mnt(C),	rc(C)) the
	      filesystem  as  appropriate.   It	  is   usually	 used	in
	      conjunction  with	mkdev hd when adding a second hard disk	to
	      the system or  with  mkdev  fd  when  creating  a	 mountable
	      filesystem  on  a	 floppy, but can be used on any	additional
	      filesystem (for example, on a large internal hard	disk).

	      /etc/mkdev fd creates bootable, root and	filesystem  floppy
	      disks.

	      Several floppies can be created during  a	 single	 mkdev	fd
	      session,	but  mkdev does	not display a prompt to	remove the
	      first floppy and insert  the  next  one.	 Insert	 the  next
	      floppy  when  mkdev  prompts  ``Would you	like to	format the
	      floppy first? (y/n).''

	      /etc/mkdev tape configures the tape  driver  in  preparation
	      for linking a new	kernel that includes tape support. It adds
	      a	standard cartridge  tape  driver,  a  mini-cartridge  tape
	      driver,  a  QIC-40  or  QIC-80 floppy tape driver, or a SCSI
	      tape driver.

	      In configuring a cartridge tape drive,  the  current  driver
	      configurations can be displayed, and changed if necessary. A
	      zero in any of the fields	 means	the  driver  automatically
	      detects  the  type  of  tape  device  installed and uses the
	      built-in values for that device.	If  the	 autoconfiguration
	      values  are  not	correct	for your tape drive, refer to your
	      hardware manual for  the	correct	 values,  reconfigure  the
	      driver and relink	the new	kernel.

	      mkdev tape can also be used to remove a tape driver from the
	      kernel.

	      /etc/mkdev shl initializes necessary devices and	configures
	      kernel parameters	associated with	the number of shell layers
	      sessions available on the	system.

	      /etc/mkdev   mouse   initializes	 necessary   devices   and
	      configures the system to use any supported mouse.

	      Once the driver is configured,  you  are	prompted  for  re-
	      linking  the  kernel.  The  appropriate  devices in /dev are
	      created.

	      The  various  init  scripts  prompt  for	 the   information
	      necessary	to create the devices.


	 Files
	      /usr/lib/mkdev/*


	 See Also
	      badtrk(ADM), divvy(ADM),	dparam(ADM),  fd(HW),  fdisk(ADM),
	      filesys(F),  format(C), hd(HW), lp(HW), mkfs(ADM), mknod(C),
	      mount(ADM), serial(HW), usemouse(C), tape(HW)

	      The System Administrator's Guide has chapters devoted to the
	      installation of most peripheral devices.


	 Value Added
	      mkdev is an extension of AT&T System V provided by the Santa
	      Cruz Operation.


							   MKDEV(ADM)