cpq_megaide-2.26i-1.ul10.i586.rpm

2.4.19-304 Errata Kernel (Service Pack 2a)

- Install/upgrade UL1.0 to UL1.0SP2a.

WARNING:

DO NOT reboot the system after installing/upgrading an existing system that is using the IDE RAID controller as a boot device until reaching step 4.

- Ensure that a megaide entry exists under the INITRD_MODULES section of /etc/sysconfig/kernel before installing the MegaIDE RPM.  If it does not then add it using similar syntax:

Example:

INITRD_MODULES="cciss reiserfs megaide"

- Install the MegaIDE RPM

# rpm –ivh cpq_megaide-2.26i-1.ul10.i586.rpm

- Reboot the system and verify that you are able to access the disk devices attached to the IDE RAID controller.

Attached is the MegaIDE RPM.

lsi_megaide-UL10-sp2a-v2.26i-1.dd

2.4.19-304 Errata Kernel (Service Pack 2a)

- Create a driver diskette from lsi_megaide-UL10-sp2a-v2.26i-1.dd

dd if=lsi_megaide-UL10-sp2a-v2.26i-1.dd of=/dev/fd0 count=1 bs=2048k

- Boot the system from the UL1.0 SP2a CD

- Press the ALT key at the boot prompt

- At the command prompt type the following:

ide-nodma acpi=oldboot

- Insert the lsi_megaide-UL10-sp2a-v2.26i-1.dd driver diskette when prompted

- Insert the UL 1.0 installation CD when prompted

- Proceed with the OS installation as normal

- Install SP2a after OS installation has completed to finish updating RPMs to the SP2a versions.  Use the /media/cdrom/install.sh to  accomplish this.